## Slide 1: Register Transfer Language and Microoperations
Unit-2

## Slide 2: Contents:
Register Transfer Language
Arithmetic Microoperations
Logic Microoperations
Shift Microoperations
Arithmetic Logic Shift Unit
Instruction codes
Computer Instructions
Instruction Cycle
Memory-Reference Instructions
Input-Output and Interrupt
Stack Organization
Instruction Formats

## Slide 3: 1. Register Transfer Language
SIMPLE DIGITAL SYSTEMS
Combinational and sequential circuits can be used to create simple digital systems.
These are the low-level building blocks of a digital computer.
Simple digital systems are frequently characterized in terms of
  the registers they contain, and
  the operations that they perform.
Typically,
  Operations are performed on the data in the registers.
  Information is passed between registers.

## Slide 4: Microoperations(1)
The operations on the data in registers are called microoperations.
The functions built into registers are examples of microoperations
  Shift
  Load
  Clear
  Increment
  …

## Slide 5: Microoperations (2)
An elementary operation performed (during one clock pulse), on the information stored in one or more registers.
R  f(R, R)
f: shift, load, clear, increment, add, subtract, complement, and, or, xor, …
ALU
(f)
Registers
(R)
1 clock cycle

## Slide 6: Organization of a Digital System
The internal organization of a computer is defined as
Set of registers and their functions.
Microoperations (Set of allowable microoperations provided by the organization of the computer).
Control signals that initiate the sequence of microoperations (to perform the functions).

## Slide 7: Register Transfer Level
Viewing a computer, or any digital system, in this way is called the register transfer level.
This is because we’re focusing on
  The system’s registers
  The data transformations in them, and
  The data transfers between them.

## Slide 8: Register Transfer Language
Rather than specifying a digital system in words, a specific notation is used called register transfer language.
For any function of the computer, the register transfer language can be used to describe the (sequence of) microoperations.
Register transfer language
  A symbolic language.
  A convenient tool for describing the internal organization of digital computers.
  Can also be used to facilitate the design process of digital systems.

## Slide 9
R1
Register
Numbering of bits
Showing individual bits
Subfields
PC(H)
PC(L)
15
8
7
0
- a register
- portion of a register
- a bit of a register
Common ways of drawing the block diagram of a register
7 6 5 4 3 2 1 0
R2
15
0
Designation of a register

## Slide 10: Basic Symbols For Register Transfers
Capital letters Denotes a register MAR, R2
& numerals
Parentheses () Denotes a part of a register R2(0-7), R2(L)
Arrow  Denotes transfer of information R2  R1
Colon : Denotes termination of control function P:
Comma , Separates two micro-operations A  B, B  A
Symbols
Description Examples

## Slide 11: 2. Arithmetic Microoperations
The microoperations most often encountered in digital computers are classified into four categories:
  Register transfer microoperations
  Arithmetic microoperations (on numeric data stored in the registers)
  Logic microoperations (bit manipulations on non-numeric data)
  Shift microoperations

## Slide 12: Arithmetic Microoperations cont.
The basic arithmetic microoperations are:
  addition
  subtraction
  increment
  decrement
  shift
Addition Microoperation:
R3 R1+R2
Subtraction Microoperation:
R3 R1-R2 (or)
R3 R1+ R2 +1
1’s complement

## Slide 13: Arithmetic Microoperations cont
One’s Complement Microoperation:
R2 R2
Two’s Complement Microoperation:
R2 R2+1
Increment Microoperation:
R2 R2+1
Decrement Microoperation:
R2 R2-1

## Slide 14: Summary of Typical Arithmetic Micro-Operations
  R3  R1 + R2 Contents of R1 plus R2 transferred to R3
  R3  R1 - R2 Contents of R1 minus R2 transferred to R3
  R2  R2 Complement the contents of R2
  R2  R2+ 1 2's complement the contents of R2 (negate)
  R3  R1 + R2+ 1 subtraction
  R1  R1 + 1 Increment
  R1  R1 - 1 Decrement
Operations
Description

## Slide 15: Arithmetic Microoperations: Binary Adder
4-bit binary adder (connection of FAs)
FA
FA
FA
FA
C0
A0
B0
S0
A1
B1
S1
A2
B2
S2
A3
B3
S3
C1
C2
C3
C4

## Slide 16
.
Arithmetic Microoperations: Binary Adder-Subtractor
FA
FA
FA
FA
C0
A0
B0
S0
A1
B1
S1
A2
B2
S2
A3
B3
S3
C1
C2
C3
C4
4-bit adder-subtractor
M

## Slide 17: Arithmetic Microoperations Binary Incrementer
C
S
x
y
HA
C
S
x
y
HA
C
S
x
y
HA
C
S
x
y
HA
S0
S1
S2
S3
C4
1
A0
A1
A2
A3
4-bit Binary Incrementer
Binary Incrementer can also be implemented using a counter.
A binary decrementer can be implemented by adding 1111 to the desired register each time.

## Slide 18: Arithmetic Microoperations Arithmetic Circuit
This circuit performs seven distinct arithmetic operations and the basic component of it is the parallel adder.
The output of the binary adder is calculated from the following arithmetic sum:
    D = A + Y + Cin

## Slide 19: Arithmetic Microoperations : Arithmetic Circuit cont.
B0
3 2 1 0 S1 S0
4×1 MUX
FA
FA
FA
FA
Cin
D0
D1
D2
D3
C1
C2
C3
Cout
B0
1
0
S1
S0
B1
3 2 1 0 S1 S0
4×1 MUX
B1
1
0
S1
S0
B2
3 2 1 0 S1 S0
4×1 MUX
B2
1
0
S1
S0
B3
3 2 1 0 S1 S0
4×1 MUX
B3
1
0
S1
S0
A0
A1
A2
A3
4-bit Arithmetic Circuit
X0
Y0
X1
Y1
X2
Y2
X3
Y3
Figure A

## Slide 20: Arithmetic Circuit
S1
S0
0
1
2
3
4x1
MUX
X0
Y0
C0
C1
D0
FA
S1
S0
0
1
2
3
4x1
MUX
X1
Y1
C1
C2
D1
FA
S1
S0
0
1
2
3
4x1
MUX
X2
Y2
C2
C3
D2
FA
S1
S0
0
1
2
3
4x1
MUX
X3
Y3
C3
C4
D3
FA
Cout
A0
B0
A1
B1
A2
B2
A3
B3
0
1
S0
S1
Cin
S1 S0 Cin Y Output Microoperation
0 0 0 B D = A + B Add
0 0 1 B D = A + B + 1 Add with carry
0 1 0 B’ D = A + B’ Subtract with borrow
0 1 1 B’ D = A + B’+ 1 Subtract
1 0 0 0 D = A Transfer A
1 0 1 0 D = A + 1 Increment A
1 1 0 1 D = A - 1 Decrement A
1 1 1 1 D = A Transfer A

## Slide 21: 3. Logic Microoperations
Specify binary operations on the strings of bits in registers
  Logic microoperations are bit-wise operations, i.e., they work on the individual bits of data.
  useful for bit manipulations on binary data .
  useful for making logical decisions based on the bit value.
There are,16 different logic functions that can be defined over two binary input variables
However, most systems only implement four of these
  AND (), OR (), XOR (), Complement/NOT
The others can be created from combination of these.
0 0 0 0 0 … 1 1 1
0 1 0 0 0 … 1 1 1
1 0 0 0 1 … 0 1 1
1 1 0 1 0 … 1 0 1
A B F0 F1 F2 … F13 F14 F15

## Slide 22: List of Logic Microoperations
- 16 different logic operations with 2 binary variables.
Truth tables for 16 functions of 2 variables and the corresponding 16 logic micro-operations
Boolean
Function
Micro-
Operations
Name
x 0 0 1 1
y 0 1 0 1
  0 0 0 0 F0 = 0 F  0 Clear
  0 0 0 1 F1 = xy F  A  B AND
  0 0 1 0 F2 = xy' F  A  B’
  0 0 1 1 F3 = x F  A Transfer A
  0 1 0 0 F4 = x'y F  A’ B
  0 1 0 1 F5 = y F  B Transfer B
  0 1 1 0 F6 = x  y F  A  B Exclusive-OR
  0 1 1 1 F7 = x + y F  A  B OR
  1 0 0 0 F8 = (x + y)' F  A  B)’ NOR
  1 0 0 1 F9 = (x  y)' F  (A  B)’ Exclusive-NOR
  1 0 1 0 F10 = y' F  B’ Complement B
  1 0 1 1 F11 = x + y' F  A  B
  1 1 0 0 F12 = x' F  A’ Complement A
  1 1 0 1 F13 = x' + y F  A’ B
  1 1 1 0 F14 = (xy)' F  (A  B)’ NAND
  1 1 1 1 F15 = 1 F  all 1's Set to all 1's

## Slide 23: Logic Microoperations
OR Microoperation
Symbol: , +
Gate:
Example: 1001102  10101102 = 11101102
P+Q: R1 R2+R3, R4 R5 R6
OR
OR
ADD

## Slide 24
Logic Microoperations
AND Microoperation
Symbol: 
Gate:
Example: 1001102  10101102 = 00001102

## Slide 25
Logic Microoperations
Complement (NOT) Microoperation
Symbol: 
Gate:
Example: 10101102 = 01010012

## Slide 26
Logic Microoperations
XOR (Exclusive-OR) Microoperation
Symbol: 
Gate:
Example: 1001102  10101102 = 11100002

## Slide 27: Hardware Implementation Of Logic Microoperations
0 0 F = A  B AND
0 1 F = AB OR
1 0 F = A  B XOR
1 1 F = A’ Complement
S1 S0
Output
-operation
Function table
B
A
S
S
F
1
0
i
i
i
0
1
2
3
4 X 1
MUX
Select

## Slide 28: 4. Shift Microoperations
There are three types of shifts
  Logical shift
  Circular shift
  Arithmetic shift
What differentiates them is the information that goes into the serial input.
Serial
input
A right shift operation
A left shift operation
Serial
input

## Slide 29: Logical Shift
In a logical shift the serial input to the shift is a 0.
A right logical shift operation:
A left logical shift operation:
In a Register Transfer Language, the following notation is used
  shl for a logical shift left
  shr for a logical shift right
  Examples:
    R2  shr R2
    R3  shl R3
0
0

## Slide 30: Circular Shift
In a circular shift the serial input is the bit that is shifted out of the other end of the register.
A right circular shift operation:
A left circular shift operation:
In a RTL, the following notation is used
  cil for a circular shift left
  cir for a circular shift right
  Examples:
    R2  cir R2
    R3  cil R3

## Slide 31: Arithmetic Shift
An arithmetic shift is meant for signed binary numbers (integer).
An arithmetic left shift multiplies a signed number by two.
An arithmetic right shift divides a signed number by two.
A right arithmetic shift operation:
A left arithmetic shift operation:
0
sign
bit
sign
bit
R n-1
R n-2
R1
R0

## Slide 32: Arithmetic Shift
In a RTL, the following notation is used
  ashl for an arithmetic shift left
  ashr for an arithmetic shift right
  Examples:
    R2  ashr R2
    R3  ashl R3

## Slide 33: Arithmetic Shifts
Shifts a signed binary number to the left or right
An arithmetic shift-left multiplies a signed binary number by 2:
ashl (00100): 01000
An arithmetic shift-right divides the number by 2.
ashr (00100) : 00010
An overflow may occur in arithmetic shift-left, and occurs when the sign bit is changed (sign reversal).

## Slide 34: Shift Microoperations
Example: Assume R1=11001110, then:
  Arithmetic shift right once : R1 = 11100111
  Arithmetic shift right twice : R1 = 11110011
  Arithmetic shift left once : R1 = 10011100
  Arithmetic shift left twice : R1 = 00111000
  Logical shift right once : R1 = 01100111
  Logical shift left once : R1 = 10011100
  Circular shift right once : R1 = 01100111
  Circular shift left once : R1 = 10011101

## Slide 35: Hardware Implementation Of Shift Microoperations
S
0
1
H0
MUX
S
0
1
H1
MUX
S
0
1
H2
MUX
S
0
1
H3
MUX
Select
0 for shift right (down)
1 for shift left (up)
Serial
input (IR)
A0
A1
A2
A3
Serial
input (IL)

## Slide 36: 5. Arithmetic Logic Shift Unit
  S3 S2 S1 S0 Cin Operation Function
  0 0 0 0 0 F = A Transfer A
  0 0 0 0 1 F = A + 1 Increment A
  0 0 0 1 0 F = A + B Addition
  0 0 0 1 1 F = A + B + 1 Add with carry
  0 0 1 0 0 F = A + B’ Subtract with borrow
  0 0 1 0 1 F = A + B’+ 1 Subtraction
  0 0 1 1 0 F = A - 1 Decrement A
  0 0 1 1 1 F = A TransferA
  0 1 0 0 X F = A  B AND
  0 1 0 1 X F = A B OR
  0 1 1 0 X F = A  B XOR
  0 1 1 1 X F = A’ Complement A
  1 0 X X X F = shr A Shift right A into F
  1 1 X X X F = shl A Shift left A into F
Arithmetic
Circuit
Logic
Circuit
C
C
4 x 1
MUX
Select
0
1
2
3
F
S3
S2
S1
S0
B
A
i
A
D
A
E
shr
shl
i+1
i
i
i
i+1
i-1
i
i

## Slide 37: 6. Instruction Codes
Instruction Code:
It is a group of bits that instruct the computer to perform a specific operation.
Operation code :
The operation code of an instruction is a group of bits that define such as
add
subtract
multiply
shift
complement.
Opcode
Address
Instruction Format

## Slide 38: The Basic Computer
The Basic Computer has two components, a processor and memory
The memory has 4096 words in it
  4096 = 212, so it takes 12 bits to select a word in memory
Each word is 16 bits long
Memory
4096X16
Opcode
Address
15
12
11
0
Instruction Format
Binary operand
15
0
Instructions
(program)
Operands
(data)
Processor register
(accumulator or AC)
Fig: Stored program organization

## Slide 39: Instruction Format
A computer instruction is often divided into two parts
  An opcode (Operation Code) that specifies the operation for that instruction
  An address that specifies the registers and/or locations in memory to use for that operation
In the Basic Computer, since the memory contains 4096 (= 212) words, we needs 12 bit to specify which memory address this instruction will use
In the Basic Computer, bit 15 of the instruction specifies the addressing mode (0: direct addressing, 1: indirect addressing)
Since the memory words, and hence the instructions, are 16 bits long, that leaves 3 bits for the instruction’s opcode.
Opcode
Address
Instruction Format
15
14
12
0
I
11
Addressing mode

## Slide 40: 7. Basic Computer Instructions
Basic Computer Instruction Format
15 14
12 11
0
I
Opcode
Address
Memory-Reference Instructions (OP-code = 000 ~ 110)
Register-Reference Instructions (OP-code = 111, I = 0)
Input-Output Instructions (OP-code =111, I = 1)
15
12 11
0
Register operation
0 1 1 1
15
12 11
0
I/O operation
1 1 1 1

## Slide 41: Basic Computer Instructions
Hex Code
Symbol I = 0 I = 1 Description
  AND 0xxx 8xxx AND memory word to AC
  ADD 1xxx 9xxx Add memory word to AC
  LDA 2xxx Axxx Load AC from memory
  STA 3xxx Bxxx Store content of AC into memory
  BUN 4xxx Cxxx Branch unconditionally
  BSA 5xxx Dxxx Branch and save return address
  ISZ 6xxx Exxx Increment and skip if zero
  CLA 7800 Clear AC
  CLE 7400 Clear E
  CMA 7200 Complement AC
  CME 7100 Complement E
  CIR 7080 Circulate right AC and E
  CIL 7040 Circulate left AC and E
  INC 7020 Increment AC
  SPA 7010 Skip next instr. if AC is positive
  SNA 7008 Skip next instr. if AC is negative
  SZA 7004 Skip next instr. if AC is zero
  SZE 7002 Skip next instr. if E is zero
  HLT 7001 Halt computer
  INP F800 Input character to AC
  OUT F400 Output character from AC
  SKI F200 Skip on input flag
  SKO F100 Skip on output flag
  ION F080 Interrupt on
  IOF F040 Interrupt off

## Slide 42: Instruction Set Completeness
Instruction Types
A computer should have a set of instructions so that the user can construct machine language programs to evaluate any function that is known to be computable.
  Functional Instructions
  - Arithmetic, logic, and shift instructions
  - ADD, CMA, INC, CIR, CIL, AND, CLA
  Transfer Instructions
  - Data transfers between the main memory
  and the processor registers
  - LDA, STA
  Control Instructions
  - Program sequencing and control
  - BUN, BSA, ISZ
  Input/Output Instructions
  - Input and output
  - INP, OUT

## Slide 43: 8. Instruction Cycle
In Basic Computer, a machine instruction is executed in the following cycle:
  Fetch an instruction from memory
  Decode the instruction
  Read the effective address from memory if the instruction has an indirect address
  Execute the instruction

## Slide 44
After an instruction is executed, the cycle starts again at step 1, for the next instruction.
Note: Every different processor has its own (different) instruction cycle .

## Slide 45: Fetch and Decode
• Fetch and Decode
T0: AR PC (S0S1S2=010, T0=1)
T1: IR  M [AR], PC  PC + 1 (S0S1S2=111, T1=1)
T2: D0, . . . , D7  Decode IR(12-14), AR  IR(0-11), I  IR(15)
S2
S1
S0
Bus
7
Memory
unit
Address
Read
AR
LD
PC
INR
IR
LD
Clock
1
2
5
Common bus
T1
T0

## Slide 46: Determine The Type Of Instruction
= 0 (direct)
D'7IT3: AR M[AR]
D'7I'T3: Nothing
D7I'T3: Execute a register-reference instr.
D7IT3: Execute an input-output instr.
Start
SC  0
AR

PC
T0
IR

M[AR],
PC

PC + 1
T1
AR

IR(0-11),
I

IR(15)
Decode Opcode in IR(12-14),
T2
D7
= 0 (Memory-reference)
(Register or I/O) = 1
I
I
Execute
register-reference
instruction
SC

0
Execute
input-output
instruction
SC

0
M[AR]

AR
Nothing
= 0 (register)
(I/O) = 1
(indirect) = 1
T3
T3
T3
T3
Execute
memory-reference
instruction
SC

0
T4

## Slide 47: Register Reference Instructions
r = D7 IT3 => Register Reference Instruction
Bi = IR(i) , i=0,1,2,...,11
- D7 = 1, I = 0
- Register Ref. Instr. is specified in b0 ~ b11 of IR
- Execution starts with timing signal T3
Register Reference Instructions are identified when
r: SC  0
CLA rB11: AC  0
CLE rB10: E  0
CMA rB9: AC  AC’
CME rB8: E  E’
CIR rB7: AC  shr AC, AC(15)  E, E  AC(0)
CIL rB6: AC  shl AC, AC(0)  E, E  AC(15)
INC rB5: AC  AC + 1
SPA rB4: if (AC(15) = 0) then (PC  PC+1)
SNA rB3: if (AC(15) = 1) then (PC  PC+1)
SZA rB2: if (AC = 0) then (PC  PC+1)
SZE rB1: if (E = 0) then (PC  PC+1)
HLT rB0: S  0 (S is a start-stop flip-flop)

## Slide 48: 9. Memory Reference Instructions
AND to AC
D0T4: DR  M[AR] Read operand
D0T5: AC  AC  DR, SC  0 AND with AC
ADD to AC
D1T4: DR  M[AR] Read operand
D1T5: AC  AC + DR, E  Cout, SC  0 Add to AC and store carry in E
- The effective address of the instruction is in AR and was placed there during
timing signal T2 when I = 0, or during timing signal T3 when I = 1
- Memory cycle is assumed to be short enough to complete in a CPU cycle
- The execution of MR instruction starts with T4
Symbol
Operation
Decoder
Symbolic Description
AND D0 AC  AC  M[AR]
ADD D1 AC  AC + M[AR], E  Cout
LDA D2 AC  M[AR]
STA D3 M[AR]  AC
BUN D4 PC  AR
BSA D5 M[AR]  PC, PC  AR + 1
ISZ D6 M[AR]  M[AR] + 1, if M[AR] + 1 = 0 then PC  PC+1

## Slide 49
Memory, PC after execution
21
0
BSA
135
Next instruction
Subroutine
20
PC = 21
AR = 135
136
1
BUN
135
Memory, PC, AR at time T4
0
BSA
135
Next instruction
Subroutine
20
21
135
PC = 136
1
BUN
135
Memory
Memory
LDA: Load to AC
D2T4: DR  M[AR]
D2T5: AC  DR, SC  0
STA: Store AC
D3T4: M[AR]  AC, SC  0
BUN: Branch Unconditionally
D4T4: PC  AR, SC  0
BSA: Branch and Save Return Address
M[AR]  PC, PC  AR + 1
Memory Reference Instructions

## Slide 50: Memory Reference Instructions
BSA:
D5T4: M[AR]  PC, AR  AR + 1
D5T5: PC  AR, SC  0
ISZ: Increment and Skip-if-Zero
D6T4: DR  M[AR]
D6T5: DR  DR + 1
D6T4: M[AR]  DR, if (DR = 0) then (PC  PC + 1), SC  0

## Slide 51: Flowchart For Memory Reference Instructions
Memory-reference instruction
DR  M[AR]
DR  M[AR]
DR  M[AR]
M[AR]  AC
SC  0
AND
ADD
LDA
STA
AC  AC DR
SC  0
AC  AC + DR
E  Cout
SC  0
AC  DR
SC  0
D T
0
4
D T
1
4
D T
2
4
D T
3
4
D T
0
5
D T
1
5
D T
2
5
PC  AR
SC  0
M[AR]  PC
AR  AR + 1
DR  M[AR]
BUN
BSA
ISZ
D T
4
4
D T
5
4
D T
6
4
DR  DR + 1
D T
5
5
D T
6
5
PC  AR
SC  0
M[AR]  DR
If (DR = 0)
then (PC  PC + 1)
SC  0
D T
6
6


## Slide 52: Basic Computer Instructions
Hex Code
Symbol I = 0 I = 1 Description
  AND 0xxx 8xxx AND memory word to AC
  ADD 1xxx 9xxx Add memory word to AC
  LDA 2xxx Axxx Load AC from memory
  STA 3xxx Bxxx Store content of AC into memory
  BUN 4xxx Cxxx Branch unconditionally
  BSA 5xxx Dxxx Branch and save return address
  ISZ 6xxx Exxx Increment and skip if zero
  CLA 7800 Clear AC
  CLE 7400 Clear E
  CMA 7200 Complement AC
  CME 7100 Complement E
  CIR 7080 Circulate right AC and E
  CIL 7040 Circulate left AC and E
  INC 7020 Increment AC
  SPA 7010 Skip next instr. if AC is positive
  SNA 7008 Skip next instr. if AC is negative
  SZA 7004 Skip next instr. if AC is zero
  SZE 7002 Skip next instr. if E is zero
  HLT 7001 Halt computer
  INP F800 Input character to AC
  OUT F400 Output character from AC
  SKI F200 Skip on input flag
  SKO F100 Skip on output flag
  ION F080 Interrupt on
  IOF F040 Interrupt off

## Slide 53: 10. Input-Output And Interrupt
Input-Output Configuration
INPR Input register - 8 bits
OUTR Output register - 8 bits
FGI Input flag - 1 bit
FGO Output flag - 1 bit
IEN Interrupt enable - 1 bit
- The terminal sends and receives serial information
- The serial info. from the keyboard is shifted into INPR
- The serial info. for the printer is stored in the OUTR
- INPR and OUTR communicate with the terminal
serially and with the AC in parallel.
- The flags are needed to synchronize the timing
difference between I/O device and the computer
A Terminal with a keyboard and a Printer
Input-output
terminal
Serial
communication
interface
Computer
registers and
flip-flops
Printer
Keyboard
Receiver
interface
Transmitter
interface
FGO
OUTR
AC
INPR
FGI
Serial Communications Path
Parallel Communications Path

## Slide 54: Input-Output Instructions
D7IT3 = p
IR(i) = Bi, i = 6, …, 11
p: SC  0 Clear SC
INP pB11: AC(0-7)  INPR, FGI  0 Input char. to AC
OUT pB10: OUTR  AC(0-7), FGO  0 Output char. from AC
SKI pB9: if(FGI = 1) then (PC  PC + 1) Skip on input flag
SKO pB8: if(FGO = 1) then (PC  PC + 1) Skip on output flag
ION pB7: IEN  1 Interrupt enable on
IOF pB6: IEN  0 Interrupt enable off

## Slide 55: Program-Controlled Input/Output
Program-controlled I/O
- Continuous CPU involvement
I/O takes valuable CPU time
- CPU slowed down to I/O speed
- Simple
- Least hardware

## Slide 56: Interrupt Initiated Input/Output
Open communication only when some data has to be passed --> interrupt.
- The I/O interface, instead of the CPU, monitors the I/O device.
- When the interface founds that the I/O device is ready for data transfer,
it generates an interrupt request to the CPU
- Upon detecting an interrupt, the CPU stops momentarily the task
it is doing, branches to the service routine to process the data
transfer, and then returns to the task it was performing.
* IEN (Interrupt-enable flip-flop)
- can be set and cleared by instructions.
- when cleared, the computer cannot be interrupted.

## Slide 57: Flowchart For Interrupt Cycle
R = Interrupt f/f
- The interrupt cycle is a HW implementation of a branch and save return address operation.
- At the beginning of the next instruction cycle, the instruction that is read from memory is in address 1.
- At memory address 1, the programmer must store a branch instruction that sends the control to an interrupt service routine.
- The instruction that returns the control to the original program is "indirect BUN 0“.
Store return address
R
=1
=0
in location 0
M[0]  PC
Branch to location 1
PC  1
IEN  0
Interrupt cycle
Instruction cycle
Fetch and decode
instructions
IEN
FGI
FGO
Execute
instructions
R  1
=1
=1
=1
=0
=0
=0
R  0

## Slide 58: Register Transfer Operations In Interrupt Cycle
Register Transfer Statements for Interrupt Cycle
- R F/F  1 if IEN (FGI + FGO)T0T1T2
 T0T1T2 (IEN)(FGI + FGO): R  1
- The fetch and decode phases of the instruction cycle
must be modified Replace T0, T1, T2 with R'T0, R'T1, R'T2
- The interrupt cycle :
RT0: AR  0, TR  PC
RT1: M[AR]  TR, PC  0
RT2: PC  PC + 1, IEN  0, R  0, SC  0
After interrupt cycle
0
BUN
1120
0
1
PC = 256
255
1
BUN
0
Before interrupt
Main
Program
1120
I/O
Program
0
BUN
1120
0
PC = 1
256
255
1
BUN
0
Memory
Main
Program
1120
I/O
Program
256

## Slide 59: 11. A Stack Machine
11/10/2022
A Stack machine has a stack as a part of the processor state
typical operations:
    push, pop, +, *, ...
Instructions like + implicitly
specify the top 2 elements of the stack as operands.
a
:
stack
Processor
Main
Store
b
a
push b

c
b
a
push c

b
a
pop

Notes: CS252 S05
59

## Slide 60: Register Stack Organization
Register Stack
Push, Pop operations
PUSH
POP
  SP  SP + 1 DR  M[SP]
  M[SP]  DR SP  SP  1
  If (SP = 0) then (FULL  1) If (SP = 0) then (EMPTY  1)
  EMPTY  0 FULL  0
Stack
- Very useful feature for nested subroutines, nested interrupt services
- Also efficient for arithmetic expression evaluation
- Storage which can be accessed in LIFO
- Pointer: SP
- Only PUSH and POP operations are applicable
A
B
C
0
1
2
3
4
63
Address
FULL
EMPTY
SP
DR
Flags
Stack pointer
stack
6 bits

## Slide 61: Memory Stack Organization
- A portion of memory is used as a stack with a processor register as a stack pointer.
- PUSH: SP  SP - 1
  M[SP]  DR
- POP: DR  M[SP]
  SP  SP + 1
Memory with Program, Data,
and Stack Segments
4001
4000
3999
3998
3997
3000
Data
(operands)
Program
(instructions)
1000
PC
AR
SP
stack
Stack grows
In this direction
- Most computers do not provide hardware to check stack overflow (full stack) or underflow (empty stack)  must be done in software

## Slide 62: Reverse Polish Notation
A + B Infix notation
+ A B Prefix or Polish notation
A B + Postfix or reverse Polish notation
- The reverse Polish notation is very suitable for stack manipulation
Evaluation of Arithmetic Expressions
Any arithmetic expression can be expressed in parenthesis-free
Polish notation, including reverse Polish notation
(3 * 4) + (5 * 6)  3 4 * 5 6 * +
Arithmetic Expressions: A + B
3
3
12
12
12
12
42
4
5
5
6
30
3
4
*
5
6
*
+

## Slide 63: Processor Organization
In general, most processors are organized in one of 3 ways
  Single register (Accumulator) organization
    Basic Computer is a good example.
    Accumulator is the only general purpose register.
  General register organization
    Used by most modern computer processors.
    Any of the registers can be used as the source or destination for computer operations.
  Stack organization
    All operations are done using the hardware stack.
    For example, an OR instruction will pop the two top elements from the stack, do a logical OR on them, and push the result on the stack.

## Slide 64: 12. Instruction Format
OP-code field - specifies the operation to be performed
Address field - designates memory address(es) or a processor register(s)
Mode field - determines how the address field is to be interpreted (to get effective address or the operand)
The number of address fields in the instruction format depends on the internal organization of CPU.
The three most common CPU organizations:
  Single accumulator organization:
  ADD X /* AC  AC + M[X] */
  General register organization:
  ADD R1, R2, R3 /* R1  R2 + R3 */
  ADD R1, R2 /* R1  R1 + R2 */
  MOV R1, R2 /* R1  R2 */
  ADD R1, X /* R1  R1 + M[X] */
  Stack organization:
  PUSH X /* TOS  M[X] */
  ADD
Instruction Fields

## Slide 65: Three, and Two-Address Instructions
Three-Address Instructions
Program to evaluate X = (A + B) * (C + D) :
ADD R1, A, B /* R1  M[A] + M[B] */
ADD R2, C, D /* R2  M[C] + M[D] */
MUL X, R1, R2 /* M[X]  R1 * R2 */
- Results in short programs
- Instruction becomes long (many bits)
Two-Address Instructions
Program to evaluate X = (A + B) * (C + D) :
MOV R1, A /* R1  M[A] */
ADD R1, B /* R1  R1 + M[A] */
MOV R2, C /* R2  M[C] */
ADD R2, D /* R2  R2 + M[D] */
MUL R1, R2 /* R1  R1 * R2 */
MOV X, R1 /* M[X]  R1 */

## Slide 66: One and Zero-Address Instructions
One-Address Instructions
- Use an implied AC register for all data manipulation
- Program to evaluate X = (A + B) * (C + D) :
LOAD A /* AC  M[A] */
ADD B /* AC  AC + M[B] */
STORE T /* M[T]  AC */
LOAD C /* AC  M[C] */
ADD D /* AC  AC + M[D] */
MUL T /* AC  AC * M[T] */
STORE X /* M[X]  AC */
Zero-Address Instructions
- Can be found in a stack-organized computer
- Program to evaluate X = (A + B) * (C + D) :
PUSH A /* TOS  A */
PUSH B /* TOS  B */
ADD /* TOS  (A + B) */
PUSH C /* TOS  C */
PUSH D /* TOS  D */
ADD /* TOS  (C + D) */
MUL /* TOS  (C + D) * (A + B) */
POP X /* M[X]  TOS */

## Slide 67
The End